## Slide 1: Embedded programing course
IoT-TLU Laboratory

## Slide 2: Get started with Raspberry pi
First Rules
Overview of Raspberry Pi
Start a Raspberry Pi
Lab #1: Controlling a LED – GPIO
Lab #2: Displaying on LCD 16x2 I2C

## Slide 3: Rules
You might actually damage hardware!
  Double check when you do wiring
  Do not connect any unintended GPIO pins, or you will short circuit the Pi
  During wiring, Power off the Pi
  Do not touch with wet fingers
  OS on SD is vulnerable. Use proper sequence to operate:
  "sudo shutdown –h now"
  "sudo reboot".
Think "why", and consult hardware reference for better understanding
Reading hardware references is a must-have skill
You don't have to read a reference thoroughly at the beginning (Later, you will)

## Slide 4: Get started with Raspberry pi
First Rules
Overview of Raspberry Pi
Start a Raspberry Pi
Lab #1: Controlling a LED – GPIO
Lab #2: Displaying on LCD 16x2 I2C

## Slide 5: Overview of Raspberry Pi
During the course, the Raspberry Pi 3 model B will be used:
  Quad Core 1.2GHz Broadcom BCM2837 64bit CPU
  1GB RAM
  BCM43438 wireless LAN and Bluetooth Low Energy (BLE) on board
  40-pin extended GPIO
  4 USB 2 ports
  4 Pole stereo output and composite video port
  Full size HDMI
  CSI camera port for connecting a Raspberry Pi camera
  DSI display port for connecting a Raspberry Pi touchscreen display
  Micro SD port for loading your operating system and storing data
  Upgraded switched Micro USB power source up to 2.5A

## Slide 6: Overview of Raspberry Pi
The Pi runs Linux – specially designed distribution called, Raspbian https://www.raspbian.org/
You download the OS image, and write on the SD on your development PC
You insert the SD into slot of the Pi, then boot up. That's all for booting Raspbian

## Slide 7: Overview of Raspberry Pi
Our devices has been pre-configured:
  Raspbian on SD card
  Keyboard mapping for US layout
  WiFi usage and IP address for 192.168.1.x/255.255.255.0 network segment, which differs on each device
  Remote X server (xrdp) waiting for a connection from your development PC
  The use of GPIO, I2C prepared
  So you can power on the Pi, and connect to the Pi using Windows Remote Desktop

## Slide 8: GPIO (GENERAL-PURPOSE INPUT/OUTPUT)
General-purpose I/O is a topic near to the hearts of the Pi, because this is the interface to the outside world.
The BCM2835 is flexibly designed to allow I/O pins to be reconfigured under software control. Ex: GPIO 14 can be an input, an output, or operate as a serial port TX data line.
One of the challenges related to the Pi’s GPIO interface is that it uses a weak CMOS 3V interface. The GPIO pins are susceptible to static electricity damage, and the I/O pins are weak drivers (2 to 16 mA). Additionally, GPIO power must be budgeted from the total spare current capacity of 50 mA

## Slide 9: GPIO Pinout Diagram

## Slide 10: Breadboard

## Slide 11: Power Supply
Unlike the normal software development, one of the often neglected, but important this is the power supply
Improper power supply make your program unstable – sudden reboot, system freeze, and unstable software
The minimum requirement for the Pi: 5V, 700mA but considering 5V, 1.2A as a minimum.
Also, depending on the peripheral connections, the more power will be required. If you use 4USB ports, provide 2.5 A
The Pi has on-board 5V regulator, which accept input from 4.75 to 5.25(V)

## Slide 12: Get started with Raspberry pi
First Rules
Overview of Raspberry Pi
Start a Raspberry Pi
Lab #1: Controlling a LED – GPIO
Lab #2: Displaying on LCD 16x2 I2C

## Slide 13: Start a Raspberry Pi
Your Pi has been configured
  WiFi IP address labeled on clear case
  Wired add 100 to your WiFi address. i.e) 192.168.1.101 => 192.168.1.201
  Keyboard English
  If you have a problem with networking, remove WiFi USB dongle, and connect LAN cable
  Then, access to the given IP address for wired network using Remote Desktop or SSH
  You cannot connect WiFi/Wired at the same time (due to the routing configuration)

## Slide 14: Get started with Raspberry pi
First Rules
Overview of Raspberry Pi
Start a Raspberry Pi
Lab #1: Controlling a LED – GPIO
Lab #2: Displaying on LCD 16x2 I2C

## Slide 15: Raspberry pi 3 - Extension

## Slide 16: Controlling a LED - Circuit
  Now you know how to create the circuit for LED
  We control LED via software, so it blinks
  In order to control the current to LED, you use GPIO of pin headers

## Slide 17: Controlling a LED - Circuit
  How to read value of a resistor
10K
1K
200

## Slide 18: Controlling a LED - Software
  Connect to the Pi via Remote Desktop, and login
  Open LXTerminal by clicking the icon of upper taskbar
  Open the "IDLE" with root privilege by:
  From menu of IDLE, select "File > New", or press CTRL+N, to open a new window

## Slide 19: Controlling a LED - Software
  Place your code in the editor
  From IDLE menu, "File > Save", or CTRL+s, to save. Name "turnON_led.py"
  Make sure your LED is still on
  "Run > Run Module", or F5, and observe the LED state

## Slide 20: Controlling a LED – Blinking LED
  Let's make the LED blinking, by changing the GPIO pin7 state
  Open the new file in IDLE
  Type as the following source code in the next slide
  Save as "blink_led.py", and run by hitting F5
  Observe the source code, to get used to Python and GPIO operation

## Slide 21: Controlling a LED – Blinking LED – Source code

## Slide 22: Assignment – “The Knight Rider”
  Put 3 LEDs, light them one by one at 0.05 second (50ms) interval. When the last LED turns off, turn on the first LED, and start the iteration again.

## Slide 23: “The Knight Rider” – How to do it?
  Use Pin 7 (GPIO04), 11 (GPIO17), 13 (GPIO27)
  You can put them in a list
  Set to the output mode by looping the pin list

## Slide 24: “The Knight Rider” – How to do it?
  Create each pattern, 3 in total, by using a list

## Slide 25: “The Knight Rider” – How to do it?
  Now execute the pattern

## Slide 26: “The Knight Rider” – How to do it?
  Now execute the pattern

## Slide 27: “The Knight Rider” – Assignment 2
  Now you have better understanding of Python, the circuit, and control theory, add two more LEDs on the circuit, and implement 5 LEDs Knight Rider and let’s user choose the direction of Knight Rider.

## Slide 28: Get started with Raspberry pi
First Rules
Overview of Raspberry Pi
Start a Raspberry Pi
Lab #1: Controlling a LED – GPIO
Lab #2: Displaying on LCD 16x2 I2C

## Slide 29: LCD 16x2

## Slide 30: Connect the LCD
  I2C (inter-integrated circuit) is also known as the two-wire interface since it only uses two wires to send and receive data. Actually it takes four if you count the Vcc and ground wires, but the power could always come from another source.
  Connecting an LCD with an I2C backpack is pretty self-explanatory. Connect the SDA pin on the Pi to the SDA pin on the LCD, and the SCL pin on the Pi to the SCL pin on the LCD. The ground and Vcc pins will also need to be connected. Most LCDs can operate with 3.3V, but they’re meant to be run on 5V, so connect it to the 5V pin of the Pi if possible.

## Slide 31: Enable I2C on the PI
  Enable I2C in Raspi-config
  First, log in to your Pi and enter sudo raspi-config to access the configuration menu. Then arrow down and select “Advanced Settings”:

## Slide 32: Enable I2C on the PI
  Enable I2C in Raspi-config
  Now arrow down and select “I2C Enable/Disable automatic loading”
  Choose “Yes” at the next prompt, exit the configuration menu, and reboot the Pi to activate the settings.

## Slide 33: Enable I2C on the PI
  Install I2C-tools and smbus
  Run command “sudo apt-get install i2c-tools” to install I2C-tools
  Run command “sudo apt-get install python-smbus” to install smbus
  Rebot Pi and login again
  Run command “i2cdetect -y 1” to detect I2C device

## Slide 34: Displaying LCD
  Install LCD library
  Run command “git clone https://anhtien17@bitbucket.org/anhtien17/lcd-master.git”
  Go to directory “lcd-master”
  Run command “sudo sh install.sh”
  Wait for Raspberry Pi re-booting
  Run demo_lcd.py